## Slide 1
AGON Light™
64.87 mm
106.05 mm
4.997 mm
103.105 mm
3.008 mm
5.056 mm
101.057 mm
53.953 mm
37.569 mm
9.024 mm
The four holes are identical. The coordinates above indicate their centers.
Hole diameter: 2.505 mm (all four), so use 2 mm screws.
The drawing above is NOT to scale.
Minimal internal case clearances:
>= 20 mm above the PCB
and
>= 10mm below the PCB
Ventilation grill required on the top of the case, especially on the right-lower side (above the voltage regulator)
See next page for connector positions!

## Slide 2
AGON Light™
64.87 mm
106.05 mm
GPIO port
ZDI port
Various ports. The back of the case should remain open for the entire length of the PCB.
16 mm
34 mm
58 mm
102 mm
The vertical clearance of all connector openings should be 20mm above the PCB.
The drawing above is NOT to scale.